## Slide 1: Chapter4 Logic Gates

## Slide 2: Objective
use the following logic gate symbols:
NOT AND OR NAND NOR XOR
understand and define the functions of NOT, AND, OR, NAND, NOR and XOR (EOR) gates, including the binary output produced from all the possible binary inputs (all gates, except the NOT gate, will have two inputs only)
construct the truth table for each of the logic gates above
construct a logic circuit from either:
– a problem statement
– a logic expression
construct a truth table from either:
– a logic circuit
– a logic expression
show understanding that some circuits can be constructed with fewer gates to produce the same outputs

## Slide 3: Boolean Constants and Variables
Boolean 0 and 1 do not represent actual numbers but instead represent the state, or logic level.
Closed switch
Open switch
Yes
No
High
Low
On
Off
True
False
Logic 1
Logic 0

## Slide 4: Three Basic Logic Operations
OR
AND
NOT

## Slide 5: AND Operation
Boolean expression for the AND operation: x =A·B
The above expression is read as “x equals A AND B”

## Slide 6: AND Gate
An AND gate is a gate that has two or more inputs and whose output is equal to the AND product of the inputs.

## Slide 7: Timing Diagram for AND Gate

## Slide 9: OR Operation
Boolean expression for the OR operation: x =A + B
The above expression is read as “x equals A OR B”

## Slide 10: OR Gate
An OR gate is a gate that has two or more inputs and whose output is equal to the OR combination of the inputs.

## Slide 11: Example
Timing diagram

## Slide 12: NOT Operation
The NOT operation is an unary operation, taking only one input variable.
Boolean expression for the NOT operation: x = A
read as “x equals the inverse of A”
Also known as inversion or complementation互补.
Can also be expressed as: A’
A
Notes: 一元的

## Slide 13: NOT Circuit
Also known as inverter.
Always take a single input
Application:

## Slide 14: Exercise 1

## Slide 15: Describing Logic Circuits Algebraically
Any logic circuits can be built from the three basic building blocks: OR, AND, NOT
  Example 1: x = A B + C
  Example 2: x = (A+B)C
  Example 3: x = (A+B)
  Example 4: x = ABC(A+D)
Notes: 代数学上

## Slide 16: Examples 1,2

## Slide 17: Examples 3

## Slide 18: Example 4

## Slide 19: Exercise 2
A car alarm is set off 触发 if a window is broken or if it senses something moving inside car, and the car is not being towed拖拽 or the engine is not on.
Where:
A = being towed,
B = window broken,
C = engine on,
D = senses movement
(B+D)·(A’+C’)

## Slide 20: Implementing Circuits from Boolean Expressions
y = AC+BC’+A’BC
x = AB+B’C
x=(A+B)(B’+C)

## Slide 22: Figure

## Slide 23: NOR Gate
Boolean expression for the NOR operation: x = A + B

## Slide 24: Figure

## Slide 25: NAND Gate
Boolean expression for the NAND operation: x = A B

## Slide 26: Figure

## Slide 27: Boolean Theorems (Multivariable)
x+y = y+x
x*y = y*x
x+(y+z) = (x+y)+z=x+y+z
x(yz)=(xy)z=xyz
x(y+z)=xy+xz
(w+x)(y+z)=wy+xy+wz+xz

## Slide 28: DeMorgan’s Theorems 狄摩根定律
(x+y)’=x’y’
Implications and alternative symbol for NOR function
(xy)’=x’+y’
Implications and alternative symbol for NAND function
Extension to N variables

## Slide 29: Figure

## Slide 30: Figure

## Slide 31: Universality of NAND Gates

## Slide 32: XOR Gate
A XOR gate takes two inputs and combines them to form one output
If exactly one input is true then the output will be true. If both the inputs are false or both the inputs are true then the output will be false.

## Slide 33: Examples of an XOR gate
(it is raining) XOR (it is not raining) = TRUE
TRUE ⊕ TRUE = FALSE
(9 < 3) ⊕ (2 < 1) = FALSE
(20 = 20) ⊕(8 > 2) = TRUE
A B out
0 0 0
0 1 1
1 0 1
1 1 0

## Slide 34: Half adder
A half adder calculates the sum and stores the value of the carry 进位 bit C as well as the result S.

## Slide 35: Truth table
a | b | c | s
0 | 0 | 0 | 0
1 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 36: Full adder

## Slide 37: Truth table