## Slide 1: 5.3 The fetch-execute cycle

## Slide 2: Objectives
describe the stages of the fetch-execute cycle
show understanding of ‘register transfer(寄存器转移)’ notation 标记
describe how to handle interrupts(中断)

## Slide 4: Interrupt
An interrupt is a signal for the CPU to stop what it is doing and instead carry out the interrupt task, once the task is complete, the CPU goes back to what it was doing.
The reasons for an interrupt：
A fatal重大 error in a program
A hardware fault
A need for I/O processing to begin
User interaction交互
A timer定时器 signal

## Slide 5: The actions of the processor when an interrupt is detected
At the end of the cycle for the current instruction the processor checks if there is an interrupt.
If the interrupt flag is set, the register contents are saved, the address of the Interrupt Service Routine (中断服务例行程序，ISR) is loaded to the Program Counter (PC) and when the ISR completes, the processor restores the register contents.

## Slide 6
This jumping of instructions from current CPU operations to the ISR and then back again is called 'context switching上下文切换'

## Slide 7: Review of Terms
A CPU contains a number of 'registers'.
A register is a small section of on-chip memory having a specific purpose.
Registers range from 8 bits wide on an 8 bit CPU to 64 bits and beyond.
PC——The Program Counter holds the address of the next instruction to be fetched.
MAR——Memory Address Register
MDR——Memory Data Register
MBR——Memory Buffer Register
CIR——Current Instruction Register

## Slide 8
PC
MAR
MDR
CIR
Memory
CPU
Copy of address of next instruction
Instruction
Copy of instruction in memory address held in MAR
PC incremented by 1
Fetch

## Slide 9
CIR
CPU
Split instruction into operation code (Opcode) and operation object (Operand). Then decode the operation code.
Decode
PC
MAR
MDR

## Slide 10
CIR
CPU
Execute instruction
Execute
PC
MAR
MDR

## Slide 11: Register transfer notation
MAR [PC]
PC [PC]+1; MDR [[MAR]]
  When two operations are placed on the same line separated隔开 by a semi-colon分号 this means that the two transfers take place发生 simultaneously同时地.
  The content of the MAR is an address; it is the content of that address which is being transferred to the MDR.
  CIR [MDR]

## Slide 12
MAR<-[PC] means obtain the content in PC, then feed it to MAR

## Slide 15
Accumulator(ACC)：intermediate 中间的 arithmetic 算术 or logic results are stored in this register

## Slide 17: The fetch-execute cycle
http://www.teach-ict.com/as_as_computing/ocr/H447/F453/3_3_3/fetch_execute_cycle/miniweb/pg4.htm

## Slide 18: Instructions
Jump
Input / Load (number directly)
Input / Load (from memory)
Store
Add (a number directly)
Add (a number from memory)
Output (directly from accumulator)
Output (from memory)

## Slide 19: Jump instruction
Execute Diagram

## Slide 20
PC
CIR
CPU
Address
Execute
Jump
MAR
MDR
Back to list of instructions

## Slide 21: Input / Load (number directly) into accumulator instruction(累计器指令)
Execute Diagram

## Slide 22
CPU
Number in MDR
Accumulator
Execute
MDR
CIR
Number inputted
Input / Load (number directly) into accumulator
PC
MAR
Back to list of instructions

## Slide 23: Load (from memory) instruction
Execute Diagram

## Slide 24
MDR
CIR
Memory
CPU
Data obtained form the address
Address of data to be loaded.
Load (from memory)
MAR
Execute
Accumulator
Data in MDR
PC
Back to list of instructions

## Slide 25: Store instruction
Execute Diagram
Assume data has either been inputted, loaded (directly or from memory) or a calculation has been performed.
Any of the above will mean there is data in the accumulator and this data will be stored.

## Slide 26
MAR
CIR
CPU
Address
to store in
Store
Execute
MDR
Memory
Put the data into the address
Accumulator
Data in accumulator
PC
Back to list of instructions

## Slide 27: Add (a number directly) instruction
Execute Diagram
Assume a number has already been inputted or loaded (directly or from memory) into the accumulator.

## Slide 28
ALU
CIR
CPU
Execute
MDR
Number to be added.
Accumulator
Add number in MDR and number already in accumulator together.
The ALU now does the arithmetic.
Accumulator value is now the result of the addition.
i.e. Accumulator = Accumulator + contents of MDR
Add (a number directly)
PC
MAR
Back to list of instructions

## Slide 29: Add (a number from memory) instruction
Execute Diagram
(Assume a number has already been inputted or loaded into the accumulator.)

## Slide 30
ALU
CIR
CPU
Address of number to be added.
Add (from memory)
Execute
MDR
Memory
Number in the memory address obtained from MAR
Accumulator
Add number in MDR to number already in accumulator.
MAR
NB. The ALU now does the arithmetic.
Accumulator value is now the result of the addition.
i.e. Accumulator = Accumulator + contents of MDR
PC
Back to list of instructions

## Slide 31: Output (directly from accumulator) instruction
Execute Diagram

## Slide 32
CPU
Accumulator
Output data
Execute
Output (directly from accumulator)
CIR
MDR
PC
MAR
Back to list of instructions

## Slide 33: Output (from memory) instruction
Execute Diagram

## Slide 34
CIR
CPU
Address of data to output.
Output (from memory)
Execute
MDR
Memory
Data in memory address held in MAR
Accumulator
Output data
Data
MAR
PC
Back to list of instructions

## Slide 35
CPU
Reset
PC
Cycle is reset by passing control signal back to the PC.

## Slide 36
Load the address of next instruction in the PC into the MAR.
  So that the control unit can fetch the instruction from the right part of the memory.
Copy the instruction/data that is in the memory address given by the MAR into the MDR.
  MDR is used whenever anything is to go from the CPU to main memory.
Increase the PC by 1.
  So that it contains the address of the next instruction, assuming that the instructions are in consecutive locations.
Load the instruction/data that is now in the MDR into the CIR.
  Thus the next instruction is copied from memory -> MDR -> CIR.
Contents of CIR split into operation code and address if present e.g. store, add or jump instructions.
Decode the instruction that is in the CIR.
Fetch
Decode

## Slide 37
Execute the instruction but what is involved in this depends on the instruction being executed (there are several different instructions you need to know about).
If the instruction is a jump instruction then
  Load the address part of the instruction in the CIR into the PC.
If the instruction is an input / load (directly) instruction then take data input and place in accumulator.
If the instruction is a load (from memory) instruction.
  Copy address part of the instruction (to load from) in the CIR into MAR.
  Copy data from memory address held in MAR to MDR.
  Copy data in MDR into accumulator.
Execute

## Slide 38
If the instruction is a store instruction then:
  Copy address part of the instruction (to store in) in the CIR into MAR.
  Copy data in accumulator to MDR.
  Copy data in MDR into memory address held in MAR.
If the instruction is an add instruction then:
  Copy address part of the instruction (of number to add) in the CIR into MAR.
  Copy number from memory address held in MAR into MDR.
  Add number in MDR to number in accumulator (accumulator will now hold the result).
If the instruction is an output (directly from accumulator) then output number in accumulator.
Execute

## Slide 39
If the instruction is an output (from memory) instruction then:
  Copy the address part of the instruction in CIR into MAR.
  Output contents of MDR.
Cycle is reset (restarted) by passing control signal back to the PC (step 1).
Execute
Reset

## Slide 40: Review

## Slide 41: 2
(a) Four points from:
The Program Counter (PC) holds the address of the next instruction to be fetched
The address in the Program Counter (PC) is copied to the Memory Address Register (MAR)
The Program Counter (PC) is incremented
The instruction is copied to the Memory Data Register (MDR) from the address held in the Memory Address Register (MAR)
The instruction from the Memory Data Register (MDR) is copied to the Current Instruction Register (CIR)

## Slide 42: 2(b)
At the end of the cycle for the current instruction B
If the interrupt flag is set, D, A and C
The interrupted program continues its execution
At the end of the cycle for the current instruction the processor checks if there is an interrupt.
If the interrupt flag is set, the register contents are saved, the address of the Interrupt Service Routine (ISR) is loaded to the Program Counter (PC) and when the ISR completes, the processor restores the register contents.